## Slide 1
INTENSIFIER
JARRING
JAR INTENSIFIER, HYDRAULIC FLUID SPRING
GENERAL DESCRIPTION
HYDRAULIC FLUID SPRING RUN WITH AN OIL JAR TO BOOST JARRING. AS THE STRING IS PULLED, A PISTON COMPRESSES A HIGHLY COMPRESSIBLE SILICONE FLUID AND STORES ENERGY JUST ABOVE THE DRILL COLLARS. WHEN THE JAR TRIPS, THIS ENERGY ACCELERATES THE COLLARS AND JAR UPWARD FOR A HIGH-IMPACT BLOW, LARGELY INDEPENDENT OF STRING DRAG OR DEPTH. IT ALSO CUSHIONS THE REBOUND AFTER EACH STROKE, AND ALLOWS FEWER DRILL COLLARS, ESPECIALLY IN SHALLOW HOLES.
TECHNICAL CHARACTERISTICS
O.D. | I.D. | Total stroke to solid | Collar weight (lb) | Tensile at yield (lb) | Torque at yield (ft-lb) | Fluid volume (gal)
1-5/8 | 1/4 | 6 | 1,100 - 1,400 | 43,200 | 260 | 0.13
1-13/16 | 5/16 | 6 | 1,360 - 1,800 | 59,400 | 340 | 0.195
2-1/4 | 3/8 | 6 | 1,560 - 2,100 | 118,500 | 1,800 | 0.211
2-29/32 | 1 | 12-3/4 | 2,200 - 3,000 | 194,800 | 2,260 | 0.692
3-1/8 | 1 | 8-3/4 | 2,400 - 3,300 | 229,200 | 4,068 | 0.375
3-3/4 | 1-1/4 | 8-1/4 | 4,200 - 5,700 | 345,000 | 7,640 | 0.82
3-3/4 | 1-1/2 | 7-7/8 | 3,400 - 4,600 | 299,700 | 5,340 | 0.63
3-3/4 | 1-7/8 | 7-5/8 | 3,500 - 4,700 | 179,500 | 2,980 | 0.613
4-1/4 | 1-15/16 | 8-5/8 | 3,500 - 4,700 | 430,300 | 9,920 | 0.92
4-1/2 | 2-3/8 | 10-3/8 | 3,600 - 4,900 | 375,000 | 11,160 | 1.15
4-3/4 | 1-1/2 | 8-7/8 | 6,300 - 8,500 | 591,900 | 18,420 | 1.0
4-3/4 | 2 | 10-1/8 | 5,600 - 7,500 | 468,800 | 17,200 | 1.35
6 | 2 | 8-5/8 | 10,200 - 13,800 | 937,000 | 34,320 | 1.57
6-1/4 | 2-1/4 | 13 | 11,800 - 16,000 | 917,400 | 40,680 | 4.24
6-3/4 | 2-3/8 | 13 | 13,000 - 17,500 | 1,013,800 | 48,660 | 3.45
7-3/4 | 3-1/16 | 13 | 11,000 - 15,000 | 1,587,900 | 64,020 | 4.65
9 | 3-3/4 | 13 | 12,000 - 16,000 | 1,621,000 | 92,260 | 3.2
Dimensions in inches. Each intensifier is matched to a jar of the same O.D. x I.D.; connections as for the matching jar. Tensile strengths are calculated theoretical yield values (about +/-20%); torque at yield is theoretical. Figures are a guide only: apply a safety factor.
DESIGN FEATURES
■ Energy storage: compressible silicone fluid acts as a spring above the collars.
■ Splined mandrel: torque transmitted in either direction, open or closed.
■ High-pressure seals: non-extrusion ring assemblies limit seal damage and wear.
■ Safe to fill and use: fluid-filled, charged with a low-pressure hand pump only.
■ Shock cushioning: absorbs rebound of the string after each jarring stroke.
OPERATING NOTES
■ String order from the fish: fishing tool, jar, drill collars, intensifier, string.
■ Stroke: 6 to 13 in under pull, depending on size.
■ No heavy weights above: no collars or heavy-weight for at least 1,000 ft above the intensifier.
■ Hot holes: above 180 F (82 C) bottom-hole temperature, bleed a little fluid before running.
HOW TO ORDER
Please specify: 1. intensifier size and the jar it matches 2. connections and O.D., if not standard 3. spares: packing sets, piston assemblies, seal rings, fill plugs, service kit 4. special intensifier fluid.