## Slide 1
JAR Z
JARRING
HYDRAULIC OIL JAR, STRAIGHT PULL
GENERAL DESCRIPTION
STRAIGHT-PULL HYDRAULIC OIL JAR FOR FISHING, DRILL STEM TESTING AND CORING. A METERING PISTON DELAYS THE STROKE WHILE THE OPERATOR TAKES STRETCH IN THE STRING, SO THE BLOW CAN BE SET FROM VERY LIGHT TO VERY HIGH IMPACT WITH NO ADJUSTMENT BEFORE OR AFTER THE RUN. THE HYDRAULIC SYSTEM IS CLOSED: OIL CANNOT ESCAPE AND WELL FLUIDS CANNOT ENTER. THE JAR RESETS WITH ONLY A FEW HUNDRED POUNDS OF WEIGHT AND TRANSMITS FULL TORQUE IN BOTH DIRECTIONS AT ALL TIMES.
TECHNICAL CHARACTERISTICS
Connection | O.D. | I.D. | Total stroke | Test pull load (lb) | Max. jarring load (lb) | Tensile at yield (lb) | Torque at yield (ft-lb) | Collar weight above jar (lb)
Sucker rod | 1-5/8 | 1/4 | 7-1/16 | 5,000 - 8,500 | 15,400 | 46,300 | 260 | 1,100 - 1,450
1-13/16 WFJ | 1-13/16 | 5/16 | 7 | 6,000 - 10,000 | 18,000 | 59,400 | 340 | 1,360 - 1,800
1-1/4 Reg | 2-1/4 | 3/8 | 6-15/16 | 7,200 - 12,000 | 21,000 | 118,500 | 1,800 | 1,560 - 2,100
2-3/8 PH-6 | 2-29/32 | 1 | 11-7/16 | 12,600 - 19,000 | 35,400 | 194,800 | 2,260 | 2,200 - 3,000
2-3/8 EUE | 3-1/16 | 1-1/2 | 11-9/16 | 12,000 - 16,000 | 27,800 | 160,200 | 2,200 | 2,300 - 3,100
2-3/8 Reg | 3-1/8 | 1 | 11-13/16 | 15,000 - 23,000 | 32,400 | 229,200 | 4,060 | 2,400 - 3,300
2-7/8 Reg | 3-3/4 | 1-1/4 | 11-13/16 | 18,000 - 26,000 | 56,500 | 345,000 | 7,640 | 4,200 - 5,700
2-3/8 IF | 3-3/4 | 1-1/2 | 12-1/8 | 15,000 - 26,000 | 46,000 | 299,700 | 5,340 | 3,400 - 4,600
2-3/8 EUE | 3-3/4 | 1-7/8 | 10-1/8 | 15,000 - 26,000 | 46,500 | 179,500 | 2,980 | 3,500 - 4,700
2-7/8 IF | 4-1/4 | 1-15/16 | 11-13/16 | 18,000 - 28,000 | 46,700 | 430,300 | 9,920 | 3,500 - 4,700
2-7/8 EUE | 4-1/2 | 2-3/8 | 12-1/4 | 18,000 - 28,000 | 49,000 | 375,000 | 11,160 | 3,600 - 4,900
3-1/2 FH | 4-3/4 | 1-1/2 | 11-13/16 | 28,000 - 45,000 | 85,000 | 591,900 | 18,420 | 6,300 - 8,500
3-1/2 FH | 4-3/4 | 2 | 13-5/16 | 28,000 - 45,000 | 74,500 | 468,800 | 17,200 | 5,600 - 7,500
4-1/2 FH | 6 | 2 | 11-7/16 | 41,000 - 62,000 | 136,400 | 937,000 | 34,320 | 10,200 - 13,800
4-1/2 IF | 6-1/4 | 2-1/4 | 14-3/8 | 55,000 - 80,000 | 159,000 | 917,400 | 40,680 | 11,800 - 16,000
5-1/2 Reg | 6-3/4 | 2-3/8 | 14-11/16 | 62,000 - 110,000 | 172,800 | 1,013,800 | 48,660 | 13,000 - 17,500
6-5/8 Reg | 7-3/4 | 3-1/16 | 14-3/8 | 63,000 - 100,000 | 149,000 | 1,587,900 | 64,020 | 11,000 - 15,000
7-5/8 Reg | 9 | 3-3/4 | 13-13/16 | 80,000 - 120,000 | 214,000 | 1,621,000 | 92,260 | 14,300 - 19,600
Dimensions in inches. Tensile strengths are calculated theoretical yield values (about +/-20%); torque at yield is the theoretical value, recommended operating torque is 50% of it. Figures are a guide only: apply a safety factor.
DESIGN FEATURES
■ Adjustable blow: impact set by the stretch taken in the string, no prior adjustment.
■ Closed hydraulic system: internal parts are constantly lubricated; no leakage in or out.
■ Easy reset: large piston ports open on closing, so only friction weight is needed.
■ Full torque: transmitted in either direction at any point of the stroke.
■ Fast repeat blows: limited only by the time to raise and lower the string.
OPERATING NOTES
■ Fishing: run directly below the drill collars; add a jar intensifier about four collars above the jar.
■ Drill stem testing, coring: 3 to 15 collars above the jar; does not interfere with test tools.
■ Never exceed the maximum jarring load. Do not tong the threaded joints; tong at least 4 in away.
■ First blow: can take seconds to minutes, depending on depth, stretch, temperature and hole condition.
HOW TO ORDER
Please specify: 1. jar size (O.D. x I.D.) 2. top and bottom connections, if not standard 3. spares: packing set, piston assembly, non-extrusion and seal protector rings, fill plugs 4. service kit and jar oil.