## Slide 1
WHIPSTOCK
WHIPSTOCK
RETRIEVABLE CASING SIDETRACK WHIPSTOCKS
GENERAL DESCRIPTION
FAMILY OF RETRIEVABLE WHIPSTOCKS USED TO SIDETRACK OUT OF CASED HOLE, FOR RE-DRILLS, RE-ENTRIES AND MULTILATERAL WINDOWS. THE WHIPSTOCK IS RUN ON A STARTER MILL TOGETHER WITH ITS ANCHORING DEVICE, ORIENTED, SET, AND THE STARTER MILL IS SHEARED OFF THE WHIP; THE WINDOW IS THEN MILLED AND POLISHED ALONG THE WHIP FACE. THREE SETTING SYSTEMS ARE COVERED: A COMBINATION PACKER AND WHIPSTOCK (SET HYDRAULICALLY, SEALS THE HOLE), AN ANCHOR AND WHIPSTOCK (SET HYDRAULICALLY, NO SEAL) AND A MECHANICALLY SET BOTTOM-TRIP WHIPSTOCK. ALL HAVE A 3 DEGREE FACE ANGLE FOR POSITIVE KICK-OFF AND CAN BE RETRIEVED IN ONE TRIP. WINDOWS CAN BE MILLED THROUGH TWO STRINGS OF CASING.
TECHNICAL CHARACTERISTICS - PACKER TYPE
Casing size | Overall length | Body Ø | Packer length | Whip face length | Face angle (°) | Wt (lb) | Bypass valve length | Bypass valve Ø | Valve wt (lb)
5-1/2 | 182 | 4-3/16 | 76 | 106 | 3 | 585 | 25 | 3-3/8 | 40
7-5/8 | 216 | 5-5/8 | 84 | 133 | 3 | 980 | 43 | 4-3/4 | 150
7-5/8 | 229 | 5-15/16 | 84 | 146 | 3 | 1,400 | 43 | 4-3/4 | 150
9-5/8 | 261 | 8-5/8 | 84 | 178 | 3 | 2,500 | 46 | 6-3/4 | 240
13-3/8 | 338 | 11-3/4 | 87 | 251 | 3 | 6,595 | 38 | 8-1/4 | 400
TECHNICAL CHARACTERISTICS - MECHANICAL BOTTOM-TRIP TYPE
Casing size | Overall length | Body Ø | Anchor length | Whip face length | Face angle (°) | Wt (lb)
5 - 5-1/2 | 142-3/8 | 4-5/16 | 35-1/8 | 74 | 3 | 570
7 | 172-1/8 | 5-7/16 | 38-1/8 | 95 | 3 | 875
8-5/8 | 189-1/2 | 7-7/16 | 43-1/2 | 124 | 3 | 1,175
Dimensions in inches, weights in lb (approximate). Packer type: bypass valve data listed separately. Bottom-trip type can also be set permanently; 7-5/8 and 9-5/8 sizes on request.
DESIGN FEATURES
■ One trip: anchor or packer, starter mill and whip run together; retrieved in one trip.
■ Anchor or packer: large slip area reduces casing stress; ratchet ring and anti-rotation keys hold the whip.
■ Shear bolt: confirms the anchor is fully set before milling starts.
■ Bottom-trip type: sets with 3,600 lb on a trigger rod; no hydraulic pressure; slips retract on retrieval.
■ Orientation: muleshoe sub, gyro or MWD.
SETTING PARAMETERS
Hydraulic set (packer, anchor) | 3,000 - 3,500 psi
Bottom-trip set, shear-down | 15,000 - 20,000 lb
Set depth | 2 - 6 ft above a casing collar
Hole angle above 4° | Set within 90° of high side
Window milling | Starter, window, watermelon mills
HOW TO ORDER
Please specify: 1. casing size and weight 2. setting system (packer, anchor or bottom-trip) 3. connections 4. orientation method.