## Slide 1
ECONOMILL
MILLING
LOW-COST LIGHT-DUTY MILL
GENERAL DESCRIPTION
LOW-COST MILLING TOOL FOR LIGHT-DUTY JOBS, DRESSED WITH TUNGSTEN CARBIDE. IT IS EFFECTIVE FOR MILLING PACKERS, RETAINERS, BRIDGE PLUGS AND CEMENT. IT HAS STANDARD API CONNECTIONS, SO IT IS MADE UP AND BROKEN OUT WITH A STANDARD BIT BREAKER AND NEEDS NO ADDITIONAL SUB. FLUID IS DIRECTED ALONG EACH CUTTING BLADE AND THROUGH THE CENTRE OF THE HEAD FOR CUTTINGS REMOVAL AND COOLING.
TECHNICAL CHARACTERISTICS
Tool series | Dressed diameter (in.) | Top pin conn. (API Reg.) | Recommended make-up torque (ft-lb) | Overall length (in.) | Wt (lb)
3000 | 3-1/4 - 4-3/8 | 2-3/8 | 3,000 - 3,500 | 7-5/8 | 17
4000 | 4-1/2 - 5-3/8 | 2-7/8 | 6,000 - 7,000 | 8-5/8 | 26
5000 | 5-1/2 - 7-3/8 | 3-1/2 | 7,000 - 9,000 | 9 | 40
7000 | 7-1/2 - 8-3/4 | 4-1/2 | 12,000 - 16,000 | 11-1/2 | 76
10000 | 10-1/4 - 12-1/4 | 6-5/8 | 28,000 - 32,000 | 16-1/2 | 125
Dimensions in inches, weights in lb (approximate). Column order follows the source layout.
DESIGN FEATURES
■ Tungsten carbide dressing: for packers, retainers, bridge plugs and cement.
■ Standard API pin connection: made up with a standard bit breaker; no extra sub needed.
■ Circulation: flow along each blade and through the head centre for cooling and cuttings removal.
■ Stabilizing ribs: above the blades, to protect the casing.
■ Cast construction: not to be used as a junk mill; cast material has lower strength.
PERFORMANCE PARAMETERS
Weight on mill | 2,000 - 8,000 lb
Practice | Light weight, low speed
Surface speed | 250 - 340 ft/min
Rotary speed | Surf. speed / (O.D. x 3.14)
If bouncing | Cut speed, then raise slowly
Stabilizer | Above mill, O.D. not larger
HOW TO ORDER
Please specify: 1. mill dressed diameter 2. size and weight of the casing to run through, if known 3. protective subs, available on request.