## Slide 1
JUNK MILL
MILLING
CONVENTIONAL JUNK MILL
GENERAL DESCRIPTION
THE WORKHORSE OF DOWNHOLE MILLING, USED TO MILL ALMOST ANYTHING IN THE HOLE INCLUDING CEMENT AND RUBBER PRODUCTS. IT IS THE ONLY TOOL ABLE TO MILL DRILL PIPE CEMENTED INSIDE AND OUT. IT IS ALSO USED TO MILL CAST-IRON BRIDGE PLUGS, AND TO MILL CASING THAT HAS BEEN MILLED TO THE POINT OF ROTATING, RUN ON A JOINT OF SLIGHTLY BENT DRILL PIPE. THREE DRESSING OPTIONS ARE LISTED: CONVENTIONAL, CONEBUSTER AND SUPER.
TECHNICAL CHARACTERISTICS
Cutting diameter (in.) | Top pin conn. (API Reg.) | Overall length: conventional and Conebuster (in.) | Overall length: Super (in.) | Fishing neck length (in.) | Fishing neck dia. (in.) | Wt (lb)
3-1/2 - 4-1/2 | 2-3/8 | 20 | 20 | 12 | 3 | 45
4-1/2 - 5-1/2 | 2-7/8 | 21 | 21 | 12 | 3-3/4 | 62
5-1/2 - 5-5/8 | 3-1/2 | 23 | 21 | 12 | 4-1/4 | 95
5-3/4 - 7-1/2 | 3-1/2 | 23 | 21 | 12 | 4-3/4 | 105
7-1/2 - 9 | 4-1/2 | 27 | 27 | 12 | 5-3/4 | 180
9-1/2 - 12-1/4 | 6-5/8 | 29 | 29 | 12 | 7-3/4 | 350
13 - 15 | 6-5/8 or 7-5/8 | 30 | 30 | 12 | 7-3/4 or 9-1/2 | 500
17 - 17-1/2 | 6-5/8 or 7-5/8 | 33 | 33 | 12 | 7-3/4 or 9-1/2 | 625
18-1/2 - 26 | 6-5/8 or 7-5/8 | 37 | 37 | 12 | 7-3/4 or 9-1/2 | 1,200
Dimensions in inches, weights in lb (approximate).
DESIGN FEATURES
■ Fishing neck: allows retrieval of the mill if it is left in the hole.
■ Dressing options: conventional, Conebuster or Super.
■ Inside casing: mill head O.D. equal to the casing drift; wear pads of the same O.D. protect the casing; stabilizer of the same O.D. run directly above.
■ Bridge plugs: mill O.D. about 1/8 in. under the plug size, to avoid skinning the casing.
OPERATING NOTES
■ Open hole: mill O.D. about 1/8 in. under hole diameter; at least 10,000 lb of drill collars; junk sub directly above the mill.
■ Spudding: frequent spudding pounds loose junk onto bottom for effective milling; a rise in torque shows junk alongside the mill.
■ Starting: set down on the junk while turning, then bring weight up; never apply weight before rotating.
PERFORMANCE PARAMETERS
Weight on mill | 4,000 - 10,000 lb
Start-up rotary speed | 60 - 80 rpm
Rotary speed once milling | 80 - 100 rpm, normal pump
Weight, second pass | 4,000 - 6,000 lb
Surface speed | 250 - 340 ft/min
Rotary speed | Surf. speed / (O.D. x 3.14)
Loose junk cycle | Mill 1-2 ft, lift 15-20 ft, settle
Stationary junk cycle | Each 3-5 ft, lift 10-15 ft, ream
Rough running | Cut speed/weight, raise slowly
Stabilizer spacing | 60 - 90 ft above mill (vertical)
HOW TO ORDER
Please specify: 1. mill diameter 2. size and weight of the casing to run through, if available 3. top connection 4. dressing (conventional, Conebuster or Super).