## Slide 1
PDM
DRILLING
POSITIVE DISPLACEMENT MOTOR WITH SLEEVE STABILIZER
GENERAL DESCRIPTION
POSITIVE DISPLACEMENT MUD MOTOR (PDM) FOR DIRECTIONAL AND PERFORMANCE DRILLING, FROM 3-1/8 TO 9-5/8 IN. IN STOCK. THE MOTOR IS BUILT FROM A POWER SECTION (ROTOR AND STATOR), AN ADJUSTABLE OR FIXED BENT HOUSING, A DRIVESHAFT ASSEMBLY, A SEALED OR MUD-LUBRICATED BEARING ASSEMBLY AND THE BIT BOX. THE BEARING HOUSING CARRIES A THREAD FOR A SCREW-ON SLEEVE STABILIZER (STRAIGHT OR SPIRAL BLADE) OR OFFSET PAD, USED TO TUNE THE BUILD RATE AND TO REDUCE LATERAL VIBRATION. SPEED IS PROPORTIONAL TO FLOW, TORQUE TO DIFFERENTIAL PRESSURE.
TECHNICAL CHARACTERISTICS
Power section OD (in) | Lobes | Stages | Max. flow (gpm) | Max. bit speed (rpm) | Std. max diff. press. (psi) | Std. torque (lb-ft) | High-power diff. press. (psi) | High-power torque (lb-ft)
3-3/8 | 7/8 | 3.0 | 120 | 188 | 460 | 782 | 690 | 1,170
3-3/4 | 6/7 | 3.0 | 200 | 160 | 440 | 1,314 | 660 | 1,970
4-3/4 | 7/8 | 2.6 | 300 | 79 | 390 | 3,500 | 590 | 5,250
5 | 6/7 | 8.0 | 350 | 302 | 1,215 | 3,500 | 1,820 | 5,250
6-1/4 | 7/8 | 2.9 | 500 | 82 | 425 | 6,277 | 640 | 9,420
6-1/2 | 8/9 | 4.0 | 500 | 145 | 605 | 4,674 | 910 | 7,010
6-3/4 | 7/8 | 5.7 | 600 | 150 | 845 | 8,204 | 1,270 | 12,310
7 | 7/8 | 7.5 | 600 | 186 | 1,120 | 8,508 | 1,680 | 12,760
7-3/4 | 7/8 | 4.0 | 900 | 149 | 570 | 8,333 | 860 | 12,500
8 | 6/7 | 5.0 | 900 | 159 | 715 | 9,618 | 1,070 | 14,430
9-5/8 | 6/7 | 6.0 | 1,200 | 155 | 880 | 15,775 | 1,320 | 23,660
11-1/4 | 6/7 | 5.6 | 1,800 | 162 | 820 | 19,377 | 1,230 | 29,070
One configuration per size: the highest-torque standard power section listed. Other lobe and stage combinations are available. High-power = enhanced elastomer power section (about 50% higher differential pressure). Values per manufacturer motor tables, for reference.
DESIGN FEATURES
■ Modular motor: power section, bent housing, driveshaft, bearing assembly and bit box can be selected to suit the job.
■ Adjustable bend: field-adjustable housing (2.38, 3 or 4 degrees) for a wide range of build rates; fixed housings on request.
■ Sleeve stabilizer option: threaded bearing housing takes a screw-on straight or spiral blade sleeve, or an offset pad.
■ Bearing assembly: oil sealed (100% of the flow to the bit) or mud lubricated.
■ Driveshaft: conventional or high-torque version for the strongest power sections.
■ Dump sub and rotor catch: bypass while tripping; retrieval of the motor after a housing failure.
PERFORMANCE PARAMETERS
Speed | Proportional to flow rate
Torque | Proportional to differential pressure, independent of flow
More torque | More stages, enhanced elastomer or even-wall stator
Stall | Standpipe pressure rises, penetration stops
If stalled | Stop rotation, slow or stop pumps, release torque slowly, lift off bottom
HOW TO ORDER
Please specify: 1. motor OD and power section (lobes, stages, standard or high-power) 2. bearing type 3. housing angle 4. sleeve stabilizer type and size, or offset pad 5. top sub / dump sub and bit box connection 6. fluid, temperature and flow range.