## Slide 1
SECTION MILL
MILLING
HYDRAULICALLY ACTUATED CASING SECTION MILL
GENERAL DESCRIPTION
HYDRAULICALLY ACTUATED TOOL THAT MILLS A SECTION OUT OF CASING OR TUBING, AND CAN ALSO BE USED TO CUT A SINGLE STRING OF CASING. PUMP PRESSURE ACROSS THE PISTON PUSHES A CAM DOWN AND EXPANDS THE KNIVES AGAINST THE CASING: THE CUT-OUT KNIVES PART THE PIPE FIRST, THEN ALL THE KNIVES TAKE PART IN MILLING. WHEN CIRCULATION STOPS, THE PISTON SPRING RETRACTS THE CAM AND THE KNIVES FOLD BACK INTO THE BODY FOR RETRIEVAL. KNIVES ARE DRESSED WITH TUNGSTEN CARBIDE INSERTS, SUITED TO POORLY CEMENTED, SPLIT OR CORRODED CASING; A SECTION OF UP TO 60 FT IS TYPICALLY MILLED WITH ONE SET OF KNIVES.
TECHNICAL CHARACTERISTICS
Tool series | Casing size | Body Ø | Fishing neck length | Fishing neck Ø | Overall length | Top pin API Reg. | Wt (lb)
3600 | 4-1/2 | 3-5/8 | 18 | 3-1/8 | 56 | 2-3/8 | 135
4100 | 5 | 4-1/8 | 18 | 3-1/4 | 66 | 2-3/8 | 175
4500 | 5-1/2, 6 | 4-1/2 | 18 | 4-1/8 | 70 | 2-7/8 | 220
5500 | 6-5/8, 7 | 5-1/2 | 18 | 4-3/4 | 74 | 3-1/2 | 350
6100 | 7-5/8 | 6-1/8 | 18 | 4-3/4 | 74 | 3-1/2 | 368
7200 | 8-5/8, 9-5/8 | 7-1/4 | 18 | 5-3/4 | 89 | 4-1/2 | 554
8200 | 9-5/8 | 8-1/4 | 18 | 5-3/4 or 8 | 87 | 4-1/2 or 6-5/8 | 900
9200 | 10-3/4, 11-3/4 | 9-1/4 | 18 | 5-3/4 or 8 | 87 | 4-1/2 or 6-5/8 | 980
11700 | 13-3/8, 16 | 11-1/2 | 18 | 8 or 9 | 90 | 6-5/8 or 7-5/8 | 1,725
Dimensions in inches, weights in lb (approximate). Standard API regular pin connections; others on request.
DESIGN FEATURES
■ Staged knife opening: three knives cut out, then all six mill.
■ Carbide cutting structure: inserts laid in a brick-work pattern for footage and penetration.
■ Positive cut-out signal: the Flo-Tel option doubles the flow area once the casing is parted, giving a 200 - 250 psi pressure drop at surface. Standard on series 4100 to 11700; not available on 3600.
■ Self-retracting: piston spring closes the knives when pumps stop.
■ Jetted top sub: limits velocity through the piston above 300 gpm.
■ Simple servicing: replaceable knives, arm-stop stabilizers and Flo-Tel unit.
FLOW RATES (GPM)
Tool series | During cut-out | During milling
3600 | 110 - 160 | 110 - 160
4100 | 80 - 125 | 110 - 160
4500 | 80 - 125 | 150 - 200
5500 | 80 - 125 | 200 - 250
6100 | 80 - 125 | 200 - 250
7200 | 80 - 125 | 200 - 300
8200 | 80 - 125 | 300 - 400
9200 | 80 - 125 | 350 - 450
11700 | 350 - 450 | 350 - 600
OPERATING PARAMETERS
Rotary speed, cut-out | 60 rpm to start
Rotary speed, milling | 80 - 120 rpm
Weight on mill | 4,000 - 8,000 lb
Min. pressure at tool | about 300 psi to cut out
Pipe cutter use | 80 - 100 rpm
HOW TO ORDER
Please specify: 1. tool series 2. size and weight of casing to be milled 3. top pin connection.