## Slide 1
TAPER MILL
MILLING
CP AND CT TAPER MILLS
GENERAL DESCRIPTION
TAPER MILLS REMOVE RESTRICTIONS AND MILL THROUGH PINCHED OR COLLAPSED CASING. THEY CARRY A TAPERED OR SHORT BLUNT NOSE THAT SERVES AS A GUIDE. TWO VERSIONS: THE CP, WITH A SHORT BLUNT NOSE AND A SHORT TAPER, PRODUCES MUCH LESS TORQUE AND CAN TAKE MORE WEIGHT, SUITING THE TOUGHEST JOBS WHERE A LONG NOSE MIGHT BREAK; THE CT, WITH SPIRAL BLADES AND A POINTED NOSE, IS DESIGNED TO MILL THROUGH RESTRICTIONS.
TECHNICAL CHARACTERISTICS
Dressed O.D. | Top pin conn. (API reg.) | Length CT | Length CP | Fishing neck length | Fishing neck O.D. | Wt CT (lb) | Wt CP (lb)
3-1/4 - 3-7/8 | 2-3/8 | 34 | 30 | 10 | 3 | 80 | 60
4 - 4-3/8 | 2-3/8 | 34 | 30 | 10 | 3-1/8 | 90 | 70
4-1/2 - 5-3/8 | 2-7/8 | 38 | 31 | 10 | 3-3/4 | 106 | 75
5-1/2 - 5-5/8 | 3-1/2 | 42 | 32 | 13 | 4-1/4 | 155 | 115
5-3/4 - 6-3/8 | 3-1/2 | 44 | 32 | 13 | 4-3/4 | 160 | 120
6-1/2 - 7-3/8 | 3-1/2 | 46 | 34 | 13 | 4-3/4 | 170 | 130
7-1/2 - 7-7/8 | 4-1/2 | 54 | 36 | 13 | 5-3/4 | 250 | 185
8-3/8 - 9-1/2 | 4-1/2 | 54 | 36 | 14 | 5-3/4 | 280 | 220
9-3/8 - 9-7/8 | 4-1/2 or 6-5/8 | 54 | 36 | 14 | 5-3/4 or 7-3/4 | 345 | 280
10-3/8 - 11 | 6-5/8 | 57 | 38 | 14 | 7-3/4 | 415 | 355
11-1/2 - 12-1/4 | 6-5/8 | 60 | 40 | 14 | 7-3/4 | 455 | 390
14-3/4 - 15 | 6-5/8 | 70 | 60 | 18 | 7-3/4 | 525 | 460
17 - 17-1/2 | 6-5/8 | 70 | 60 | 18 | 7-3/4 | 595 | 530
20 - 26 | 6-5/8 or 7-5/8 | 76 | 66 | 18 | 7-3/4 or 9-1/2 | 1,250 | 1,125
Dimensions in inches (overall lengths in inches), weights in lb (approximate). Ranges as dressed diameters of each size group.
DESIGN FEATURES
■ CP: blunt nose, short taper; low torque, tolerates more weight.
■ CT: spiral blades and pointed nose for restrictions.
■ Typical jobs: reaming collapsed casing and liners, cleaning permanent whipstock windows, milling jagged or split shoes, enlarging restrictions through retainers and adapters.
■ Stabilising: keep 1/2 to 1 in. under drift diameter.
OPERATING PARAMETERS
Weight range (general) | 2,000 - 4,000 lb
Start rotation above collapse | 75 rpm (min. 75 rpm)
Weight increase in collapse | 1,000 - 2,000 lb, slowly
Collapsed casing | about 50 rpm; 2,000 - 3,000 lb
Whipstock window clean-up | 40 rpm; under 1,000 lb
Retainers / adapters | about 70 rpm; 2,000 - 6,000 lb
After clearing restriction | 80 - 100 rpm
OPERATING NOTES
Run a mill about 1/4 in. larger than the minimum I.D. of the collapse and enlarge in stages; do not use a taper mill if the collapse has passed centre. A string taper mill can be used if there is a danger of sidetracking. Governing factor is torque: reduce speed and weight if it rises. For a window, run the same diameter as the largest window mill, rotate slowly its full length and repeat until torque is minimal; do not try to make hole.
HOW TO ORDER
Please specify: 1. type (CP or CT) 2. dressed diameter 3. top pin connection 4. fishing neck diameter, if different from standard.