## Slide 1
Drilling Jar
JARRING
DOUBLE-ACTING HYDRAULIC / MECHANICAL DRILLING JAR
GENERAL DESCRIPTION
HYDRAULIC-DELAY JAR FOR BOTH UPSTROKE AND DOWNSTROKE, WITH A MECHANICAL LATCH, BUILT FOR COMPLEX DRILLING PROGRAMS. THE DOWNSTROKE DELAY MAKES IT EFFECTIVE IN DIRECTIONAL, HORIZONTAL AND EXTENDED-REACH WELLS. BECAUSE NO BLEED-THROUGH OPERATION IS NEEDED WHEN TAGGING OR PICKING UP OFF BOTTOM, IT CAN BE PLACED IN COMPRESSION IN THE DRILLSTRING. LATCH RELEASE SETTINGS ARE ADJUSTABLE.
TECHNICAL CHARACTERISTICS
Tool O.D. (in) | 4-1/4 | 4-3/4 | 6-1/4 | 6-1/2 | 6-3/4 | 7 | 8 | 9-1/2
Tool O.D. (mm) | 108 | 121 | 159 | 165 | 171 | 178 | 203 | 241
Inside Ø (in) | 2 | 2-1/4 | 2-1/4 | 2-1/4 | 2-1/2 | 2-1/2 | 2-13/16 | 3
Max. hole Ø (in)* | 6-1/4 | 7-7/8 | 12-1/4 | 12-1/4 | 12-1/4 | 12-1/4 | 17-1/2 | 26
Max. jar load (lbf) | 86,000 | 84,000 | 160,000 | 160,000 | 190,000 | 190,000 | 300,000 | 350,000
Tensile yield (lbf) | 350,000 | 362,000 | 755,000 | 755,000 | 823,000 | 1,000,000 | 1,000,000 | 1,225,000
Torsional yield (lbf-ft)** | 11,500 | 11,500 | 37,500 | 37,500 | 44,500 | 70,000 | 73,500 | 95,000
Total stroke (in) | 17.5 | 19 | 22 | 22 | 20 | 20 | 21 | 21
Std up latch (lbf) | 35,000 | 40,000 | 90,000 | 90,000 | 90,000 | 90,000 | 95,000 | 100,000
Max. up latch (lbf) | 50,000 | 55,000 | 140,000 | 140,000 | 140,000 | 140,000 | 150,000 | 155,000
Std down latch (lbf)*** | 15,750 | 18,000 | 40,500 | 40,500 | 40,500 | 40,500 | 42,750 | 45,000
Max. down latch (lbf) | 22,500 | 27,000 | 63,000 | 63,000 | 63,000 | 63,000 | 67,500 | 69,800
Pump open area (in²) | 5.4 | 6.5 | 9.6 | 9.6 | 11.0 | 11.0 | 14.2 | 15.9
Length, latched (ft) | 22 | 19.8 | 22.5 | 22.5 | 23.0 | 23.0 | 22.5 | 23.0
Weight (lb) | 730 | 850 | 2,000 | 2,100 | 2,300 | 2,500 | 3,100 | 5,200
Ref. | 4525 | 431 | 442 | 428 | 440 | 480 | 411 | 437
* Hole openers not recommended. ** Rating based on the yield of the body connections, independent of tool-joint connections. *** Down latch setting is 45% of the up latch setting, tolerance +/- 5.
DESIGN FEATURES
■ Delay in both directions: hydraulic delay with mechanical latch, upstroke and downstroke.
■ Adjustable latch: release settings can be changed up to the maximum values above.
■ Jet-type metering device controls the hydraulic delay.
■ Safe on the rig floor: no unexpected jarring while making connections or drilling.
■ Simple to operate: no torque needed in the jarring procedure.
■ Built for high friction: weight can be stacked before firing, even in horizontal sections.
■ Consistent firing: continuous, repeatable jarring performance.
OPERATING PARAMETERS
Placement in string | Tension, neutral or compression
Delay | Hydraulic, up and down
Torque for jarring | None required
Tagging / picking up | No bleed-through needed
Down latch | 45% of up latch, +/- 5
Hole openers | Not recommended
HOW TO ORDER
Please specify: 1. tool O.D. and ref. 2. top and bottom connections 3. up and down latch release settings (standard or adjusted, within the maximum) 4. hole diameter and drilling program (directional, horizontal or extended reach).