## Slide 1
Overshot
FISHING
SERIES 150 RELEASING AND CIRCULATING OVERSHOT
GENERAL DESCRIPTION
EXTERNAL-CATCH FISHING TOOL THAT ENGAGES, PACKS OFF AND PULLS TWISTED-OFF OR LOST TUBING, DRILL PIPE, COUPLINGS, TOOL JOINTS, CASING AND OTHER SMOOTH-O.D. FISH. A SPIRAL OR BASKET GRAPPLE GRIPS THE FISH OVER A LONG SECTION, SO HEAVY PULLING, TORSION AND JARRING LOADS ARE TAKEN WITHOUT DAMAGING THE TOOL OR THE FISH. ENGAGING AND RELEASING BOTH USE RIGHT-HAND ROTATION ONLY.
FULL STRENGTH SIZES
Overshot O.D. | Max. catch, spiral | Max. catch, basket | Type | Wt (lb)*
3-5/8 | 2-1/2 | 2 | FS | 55
4-1/8 | 3-1/8 | 2-5/8 | FS | 70
5-9/16 | 4-1/4 | 3-11/16 | FS | 130
5-5/8 | 4-5/8 | 4-1/8 | FS | 130
5-3/4 | 4-3/4 | 4-1/4 | FS | 138
7-7/8 | 6-1/4 | 5-1/2 | FS | 261
8-1/8 | 6-1/2 | 5-3/4 | FS | 274
8-1/4 | 6-5/8 | 5-7/8 | FS | 280
9-5/8 | 8 | 7-1/4 | FS | 337
10-1/8 | 8-1/2 | 7-3/4 | FS | 358
10-5/8 | 9 | 8-1/4 | FS | 401
11-1/4 | 9-5/8 | 8-7/8 | FS | 520
11-3/4 | 10-1/8 | 9-3/8 | FS | 642
* Assembly dressed with spiral parts. Inches. FS = full strength. Slim-hole and semi full strength types also exist; undersize parts fit smaller fish.
WIDE CATCH VERSION
Tool O.D. | Catch range | Max. catch, spiral | Max. catch, basket | Load, spiral (lb)
4-11/16 | 1/4 | 3-21/32 | 3-1/16 | 332,100
5-3/4 | 5/16 | 4-3/4 | 4-1/8 | 407,100
7-3/8 | 3/16 | 6-1/2 | 5-7/8 | 435,200
8-1/8 | 5/16 | 7 | 6-1/4 | 548,900
9-1/8 | 5/16 | 8 | 7-1/4 | 548,900
11-3/4 | 1/2 | 10-1/8 | 9 | 969,000
Same design with an extended catch range, up to four times that of a standard overshot, to reach heavily worn fish. Standard or high-pressure seals, full flow through the fish, coarse top-sub threads with set screws, 18 in. fish neck. Can cut grapple inventory by up to 75%.
DESIGN FEATURES
■ Spiral or basket grapple: spiral for fish near maximum catch size, basket for smaller fish.
■ Pack-off: sleeve packer with spiral grapple; double-lip mill control packer (field-replaceable seals) with basket grapple.
■ Circulation through the fish to help free it.
■ Right-hand only: no left-hand rotation to engage or release.
■ Accessories: oversize, wall hook and mill guides, extension subs, lock rings; coarse-thread version for easier assembly.
OPERATION
■ Engage: rotate slowly right while lowering over the fish, let the twist slack out, then pull.
■ If the fish stays: start the pumps and keep an upward strain.
■ Release: bump down, then rotate right while slowly raising.
■ Precautions: stop the pumps before lowering over the fish; bump full string weight before releasing; no left-hand rotation without upward strain.
HOW TO ORDER
Please specify: 1. tool name and assembly number 2. size and type of fish 3. top connection 4. O.D. if other than standard. Spares (spiral): 3 packers, 2 grapples per size, 1 control. Spares (basket): 2 grapples, mill control packers per size.