## Slide 1
Spear
FISHING
FULL CIRCLE RELEASING SPEAR
GENERAL DESCRIPTION
INTERNAL-CATCH FISHING SPEAR FOR TUBING, DRILL PIPE AND CASING OF ALL SIZES. FULL CIRCLE SLIPS AND THE TAPERS ON THE BODY SPREAD THE EXPANSION STRAIN OVER A LONG VERTICAL SECTION AND ALMOST THE WHOLE INNER CIRCUMFERENCE OF THE FISH, ALLOWING HEAVY PULLING AND JARRING WITHOUT DISTORTING IT. CAN BE RUN WITH INTERNAL CUTTERS FOR CUT-AND-PULL OPERATIONS.
DRILL PIPE AND TUBING
Spear size | Slips Ø retracted | Slip area (sq in) | Wt (lb) | Body yield (lb)
2-3/8 DP | 1-11/16 | 55 | 32 | 56,400
2-3/8 Tbg | 1-29/32 | 59 | 40 | 71,500
2-7/8 DP | 2 | 74 | 55 | 110,400
2-7/8 Tbg | 2-5/16 | 87 | 60 | 134,000
3-1/2 DP | 2-7/16 | 95 | 71 | 172,000
3-1/2 Tbg | 2-13/16 | 115 | 92 | 224,000
4 DP | 3-3/32 | 126 | 107 | 296,000
4 Tbg | 3-5/16 | 135 | 127 | 275,000
4-1/2 DP | 3-15/32 | 178 | 180 | 318,000
5-1/2 DP | 4-1/2 | 265 | 270 | 628,000
CASING
Spear size | Slips Ø retracted | Slip area (sq in) | Wt (lb) | Body yield (lb)
4-1/2 | 3-25/32 | 210 | 132 | 376,000
5 | 4 | 217 | 169 | 454,000
5-1/2 | 4-1/2 | 265 | 226 | 628,000
6 | - | 315 | 283 | 945,000
6-5/8 | 5-1/2 | 350 | 358 | 1,060,000
7 | 5-3/4 | 365 | 398 | 1,228,000
7-5/8 | 6-7/16 | 430 | 502 | 1,414,000
8-5/8 | 7-1/4 | 485 | 652 | 1,761,000
9-5/8 | 8-3/16 | 580 | 833 | 2,324,000
10-3/4 | 9-1/2 | 690 | 1,240 | 3,300,000
11-3/4 | 10-9/16 | 785 | 1,552 | 4,300,000
13-3/8 | 12 | 890 | 2,017 | 5,961,000
Dimensions in inches. DP: drill pipe, Tbg: tubing. Yield strengths are theoretical body values (accuracy about 20%), not the strength of the fish; jarring may multiply the pull load by 3 to 10. Each spear has 3 to 6 slips depending on size.
DESIGN FEATURES
■ Full circle slips: large engagement area, low risk of rupturing the fish.
■ Friction grip: friction springs up to 3-1/2 in. nominal and 4 in. tubing; friction blocks on larger sizes and casing.
■ Safety ring: stops the spear entering a fish too small to release from.
■ Two release modes: bump down and rotate; left-hand wickers on the slips as back-up.
■ Circulation: safety ring packoff seals inside the fish.
ACCESSORIES
Mill, side hill and sub-type nuts; 36 in. extensions (bored for circulation); skirts and guides for oversize holes; stop subs.
OPERATION
■ Engage: lower slowly into the fish, rotate at least 1/6 turn to the left, then pull.
■ Release: bump down full string weight, rotate at least 1/6 turn to the right and raise.
■ Deep or crooked holes: more rotation may be needed; it does no harm.
■ Always keep a heavy upward strain when rotating the fish, and bump down before releasing.
HOW TO ORDER
Please specify: 1. spear name and assembly number 2. size and type of top connection 3. size and weight of the pipe to be caught. Recommended spares: 2 sets of slips per fish size, 1 unitizer (or 2 friction block assemblies), 2 friction retainers, 1 stop, 1 safety ring per slip size.