## Slide 1
VENTURI BASKET
FISHING
VENTURI JUNK BASKET
GENERAL DESCRIPTION
JUNK RETRIEVAL TOOL FOR COILED TUBING. FLUID PUMPED THROUGH THE STRING AND OUT OF NOZZLES IN THE VENTURI CHAMBER CREATES A VACUUM THAT DRAWS FLUID AND DEBRIS IN AT THE BOTTOM OF THE TOOL AND BACK UP THROUGH THE VENTURI TUBES; MOST OF IT MIXES WITH THE PRESSURIZED FLOW AND RECIRCULATES AROUND THE BOTTOM. IN EFFECT A HIGH-POWERED VACUUM CLEANER, IT WORKS WITH FLUID, MULTIPHASE FLUID, FOAM OR GAS. A HOLLOW MAGNETIC SECTION WITH A FINGER-TYPE TRAP HOLDS THE JUNK INSIDE THE TOOL, AND IT DOES NOT DEPEND ON HOLE SIZE: A 3-1/8 IN. OD TOOL CAN CLEAN UP 7 IN. CASING.
TECHNICAL CHARACTERISTICS
Size (OD) | ID | Top connection | Length | Tensile strength
1-3/4 | 0.469 | 1 AMMT box | 33 | 36,000 lb
2-1/16 | 1 | 1-1/2 AMMT box | 33 | 45,840 lb
2-1/4 | 1 | 1-1/2 AMMT box | 33 | 45,840 lb
2-5/8 | 1 | 1-1/2 AMMT box | 36-5/8 | 45,840 lb
3-1/8 | 1 | 2-3/8 PAC pin | 42 | 109,600 lb
3-1/8 | 1 | 2-3/8 REG box | 42 | 109,600 lb
Dimensions in inches. All sizes: operating pressure 5,000 psi, temperature rating 0 to 350 F, standard nozzle 0.062 in.
DESIGN FEATURES
■ Venturi suction: nozzles create a vacuum that pulls fluid and debris into the tool from the bottom.
■ Interchangeable nozzles: changed out to suit the available pump rate, fluid or gas.
■ Debris filter screen: placed before the venturi chamber to keep debris out of the venturi tubes.
■ Magnetic trap: hollow magnetic section with a finger-type trap retains junk; debris is carried out of the well inside the tool.
■ Barrel extensions: extension tubes increase the volume of junk the tool can carry.
■ Hole size independent: works in holes much larger than the tool OD.
HOW TO ORDER
Please specify: 1. tool size and top connection 2. nozzle size for the pump rate and fluid 3. extension tube length(s) for the junk volume to be carried 4. service kit.
OPTIONAL NOZZLES
Nozzle sizes (in.) | 0.062 (std), 0.078, 0.094, 0.109, 0.125, 0.140, 0.156, 0.171, 0.187
Applies to | All sizes, 1-3/4 to 3-1/8 (two nozzle series: 1-3/4 to 2-1/4 and 2-5/8 to 3-1/8)
EXTENSION TUBES
Tool size | Extension tube lengths (ft)
1-3/4 | 4, 6
2-1/16 | 4, 6
2-1/4 | 4
2-5/8 | 2, 4, 5, 5
3-1/8 | 4, 10
OPERATING PARAMETERS
Fluids | Fluid, multiphase fluid, foam, gas
Pressure | 5,000 psi
Temperature | 0 to 350 F